## Slide 1
ERROR DETECTION
&
ERROR CORRECTION

## Slide 2
Data can be corrupted during transmission
For reliable communication, errors must be detected and corrected.
Error detection and correction are implemented either at data link layer or at the transport layer of the OSI model.

## Slide 3: TYPES OF ERRORS
Single bit error :-
- Only one bit in the data unit has changed.
Burst error :-
- It means that two or more bits in the data unit has changed.

## Slide 4: Single bit Error
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
Burst Error
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0 changed to 1
Received
Sent
Sent
Received
Bits corrupted by Burst Error

## Slide 5: ERROR DETECTION
Error detecting code is to include only enough redundancy to allow the receiver to deduce that an error occurred, but not which error, and have it request a re-transmission.
Error detection uses the concept of redundancy, which means adding extra bits for detecting error at the destination.

## Slide 6: Redundancy
Instead of repeating the entire data stream, a shorter group of bits may be appended to the end of each unit.
This technique is called Redundancy because the extra bits are redundant to the information.
They are discarded as soon as the accuracy of the transmission has been determined.

## Slide 8
There are basically four types of redundancy checks. They are:
1. VRC (Vertical Redundancy Check).
2. LRC (Longitudinal Redundancy Check).
3. CRC (Cyclical Redundancy Check).

## Slide 9
VERTICAL REDUNDANCY CHECK
It is also known as Parity Check
Least expensive mechanism for error detection
In this technique, the redundant bit called parity bit is appended to every data unit so that the total number of 1s in the unit becomes even (including parity bit)

## Slide 10
VERTICAL REDUNDANCY CHECK
Checking function
Is total number
of 1s even ?
Receiver
1100001 | 1
Even – parity
generator
1100001
1
Data
VRC
Sender

## Slide 11: VERTICAL REDUNDANCY CHECK
Example :
1110110 1101111 1110010
- After adding the parity bit
11101101 11011110 11100100

## Slide 12: VERTICAL REDUNDANCY CHECK
VRC can detect all single-bit errors
  It can detect burst errors if the total number of errors in each data unit is odd.
VRC can not detect errors where the total number of bits changed is even.

## Slide 13
LONGITUDINAL REDUNDANCY CHECK (LRC)
In this method, a block of bits is organized in table(rows and columns)
Calculate the parity bit for each column and the set of these parity bits is also send with original data.
From the block of parity we can check the redundancy.

## Slide 14: LRC Example
11100111 11011101 00111001 10101001
11100111 11011101 00111001 10101001
11100111 1101101 00111001 10101001 10101010
11100111
11011101
00111001
10101001
LRC
10101010
Original data plus LRC

## Slide 15
Advantage :
-> LRC of n bits can easily detect burst error of n bits.
Disadvantage :
-> If two bits in one data unit are damaged and two bits in exactly same position in another data unit are also damaged , the LRC checker will not detect the error.

## Slide 16: CYCLIC REDUNDANCY CHECK (CRC)
In this method , a sequence of redundant bits , called the CRC or the CRC remainder, is appended to the end of the unit so that the resulting data unit become exactly divisible by a second, predetermined binary number.
At its destination, the incoming data unit is divided by the same number.
If at this step there is no remainder ,the data unit assume to be correct and is accepted, otherwise it indicate that data unit has been damaged in transmission and therefore must be rejected.
The redundancy bits used by CRC are derived by dividing the data unit by a predetermined divisor. The remainder is the CRC.

## Slide 17
CRC Generator And Checker
DATA
CRC
DIVISOR
REMAINDER
CRC
DATA
CRC
DIVISOR
DATA
00…0
Zero  Accept
Nonzero  Reject
N bits
N+1 bits
N bits
Receiver
Sender

## Slide 18
Divisor
The divisor is determined according to the algebraic polynomial.
for e.g.
A polynomial is
X^7 + x^5 + x^2 + x + 1
generation of divisor from polynomial
X^7 + X^5 + X^2 + X + 1
1 0 1 0 0 1 1 1
X^4 X^3
X^6

## Slide 19
A polynomial should be selected according to the following rule:-
It should not be divisible by x.
It should be divisible by x+1.
CRC

## Slide 20
Example :-
The CRC generator at sender end :
1 1 0 1
1 1 1 1 0 1
1 0 0 1 0 0
0 0 0
1 1 0 1
1 0 0 0
1 1 0 1
1 0 1 0
1 1 0 1
1 1 1 0
1 1 0 1
0 1 1 0
0 0 0 0
1 1 0 0
1 1 0 1
0 0 1

## Slide 21
The CRC checker at receiver end :
1 1 0 1
1 1 1 1 0 1
1 0 0 1 0 0
0 0 1
1 1 0 1
1 0 0 0
1 1 0 1
1 0 1 0
1 1 0 1
1 1 1 0
1 1 0 1
0 1 1 0
0 0 0 0
1 1 0 1
1 1 0 1
0 0 0

## Slide 22: ERROR CORRECTION
Error correcting code is to include enough redundant information along with each block of data sent to enable the receiver to deduce what the transmitted character must have been.
Error Correction must be handled in two ways :
- When an error is discovered, the receiver can have the sender retransmit the entire data unit.
- Receiver can use an error correcting code, which automatically corrects certain errors.

## Slide 23
There are two types of Error Correcting techniques :
1. Single bit error correction.
2. Burst error correction.
Error Correction can be done with the help
of HAMMING CODE.

## Slide 24: HAMMING CODE
Technique developed by R.W.Hamming.
Hamming code can be applied to data units of any length and uses the relationship between data and redundancy bits. For eg.:

## Slide 25
A 7 bit ASCII code requires 4 Redundancy bits that can be added to the end of the data unit or interspersed with the original data bits.
These bits are placed in positions 1,2,4 and 8. We refer to these bits as r1,r2,r4 and r8.

## Slide 26
d | d | d | r | d | d | d | r | d | r | r
Redundancy Bits
Positions of Redundancy Bits in Hamming Code
11
10
9
8
7
6
5
4
3
2
1

## Slide 27
In the Hamming code, each r bit is the VRC bit for one combination of data bits :
- r1 is the one combination of data bits.
- r2 is another combination of data bits.
and so on.
The combination used to calculate each of the four values for a 7 bit data sequence are as follows :
- r1 : bits 1,3,5,7,9,11.
- r2 : bits 2,3,6,7,10,11.
- r4 : bits 4,5,6,7.
- r8 : bits 8,9,10,11.

## Slide 28
1 | 0 | 0 |  | 1 | 1 | 0 |  | 1 |  | 
1 | 0 | 0 |  | 1 | 1 | 0 |  | 1 |  | 1
1 | 0 | 0 |  | 1 | 1 | 0 |  | 1 | 0 | 1
1 | 0 | 0 |  | 1 | 1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1
Data : 1 0 0 1 1 0 1
Data
Adding r1
Adding r2
Adding r4
Adding r8
Code : 1 0 0 1 1 1 0 0 1 0 1
11
10
9
8
7
6
5
4
3
2
1

## Slide 29
1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1
Sent
Received
Error

## Slide 30
1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1
11
10
9
8
7
6
5
4
3
2
1
1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1
11
10
9
8
7
6
5
4
3
2
1
1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1
11
10
9
8
7
6
5
4
3
2
1
1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1
11
10
9
8
7
6
5
4
3
2
1
0
1
1
1
The bit in position 7 is in error