## Slide 1: Design Patterns

## Slide 2: Design Patterns
In software engineering, a design pattern is a general repeatable solution to a commonly occurring problem in software design.
A design pattern isn't a finished design that can be transformed directly into code.
It is a description or template for how to solve a problem that can be used in many different situations.

## Slide 3: Uses of Design Patterns
Design patterns can speed up the development process by providing tested, proven development paradigms.
Reusing design patterns helps to prevent subtle issues that can cause major problems and improves code readability for coders and architects familiar with the patterns.
Design patterns provide general solutions, documented in a format that doesn't require specifics tied to a particular problem.
Design patterns allow developers to communicate using well-known, well understood names for software interactions.
Common design patterns can be improved over time, making them more robust than ad-hoc designs.

## Slide 4: Categories of Design Patterns
Creational design patterns | Structural design patterns | Behavioural design patterns
Abstract Factory | Adapter | Chain of responsibility
Builder | Bridge | Command
Factory Method | Composite | Interpreter
Object Pool | Decorator | Iterator
Prototype | Facade | Mediator
Singleton | Flyweight | Memento
 | Private Class Data | Null Object
 | Proxy | State
 |  | Strategy
 |  | Observer
 |  | Template method
 |  | Visitor

## Slide 5: Creational design patterns
These design patterns are all about class instantiation.
This pattern can be further divided into class-creation patterns and object-creational patterns.
Class-creation patterns use inheritance effectively in the instantiation process.
Object-creation patterns use delegation effectively to get the job done.

## Slide 6: Creational design patterns
In software engineering, creational design patterns are design patterns that deal with object creation mechanisms, trying to create objects in a manner suitable to the situation.
The basic form of object creation could result in design problems or added complexity to the design. Creational design patterns solve this problem by somehow controlling this object creation.

## Slide 7: Abstract Factory
Creates an instance of several families of classes.
Provide an interface for creating families of related or dependent objects without specifying their concrete classes.
A hierarchy that encapsulates: many possible "platforms", and the construction of a suite of "products".
The ”new” operator considered harmful.

## Slide 8: Abstract Factory
If an application is to be portable, it needs to encapsulate platform dependencies.
These "platforms" might include: windowing system, operating system, database, etc.
Too often, this encapsulation is not engineered in advance, and lots of #ifdef case statements with options for all currently supported platforms begin to procreate like rabbits throughout the code.

## Slide 9: Abstract Factory
Provide a level of indirection that abstracts the creation of families of related or dependent objects without directly specifying their concrete classes.
The "factory" object has the responsibility for providing creation services for the entire platform family. Clients never create platform objects directly, they ask the factory to do that for them.
This mechanism makes exchanging product families easy because the specific class of the factory object appears only once in the application - where it is instantiated.
The application can wholesale replace the entire family of products simply by instantiating a different concrete instance of the abstract factory.
Because the service provided by the factory object is so pervasive, it is routinely implemented as a Singleton.

## Slide 10: Abstract Factory
The Abstract Factory defines a Factory Method per product. Each Factory Method encapsulates the new operator and the concrete, platform-specific, product classes. Each "platform" is then modeled with a Factory derived class.

## Slide 11: Abstract Factory
The purpose of the Abstract Factory is to provide an interface for creating families of related objects, without specifying concrete classes.
This pattern is found in the sheet metal stamping equipment used in the manufacture of Japanese automobiles.
The stamping equipment is an Abstract Factory which creates auto body parts.
The same machinery is used to stamp right hand doors, left hand doors, right front fenders, left front fenders, hoods, etc. for different models of cars.
Through the use of rollers to change the stamping dies, the concrete classes produced by the machinery can be changed within three minutes.

## Slide 12: Abstract Factory
Check list
  Decide if "platform independence" and creation services are the current source of pain.
  Map out a matrix of "platforms" versus "products".
  Define a factory interface that consists of a factory method per product.
  Define a factory derived class for each platform that encapsulates all references to the new operator.
  The client should retire all references to new, and use the factory methods to create the product objects.

## Slide 13: Abstract Factory
Rules of thumb
  Sometimes creational patterns are competitors: there are cases when either Prototype or Abstract Factory could be used profitably. At other times they are complementary: Abstract Factory might store a set of Prototypes from which to clone and return product objects, Builder can use one of the other patterns to implement which components get built. Abstract Factory, Builder, and Prototype can use Singleton in their implementation.
  Abstract Factory, Builder, and Prototype define a factory object that's responsible for knowing and creating the class of product objects, and make it a parameter of the system. Abstract Factory has the factory object producing objects of several classes. Builder has the factory object building a complex product incrementally using a correspondingly complex protocol. Prototype has the factory object (aka prototype) building a product by copying a prototype object.
  Abstract Factory classes are often implemented with Factory Methods, but they can also be implemented using Prototype.
  Abstract Factory can be used as an alternative to Facade to hide platform-specific classes.
  Builder focuses on constructing a complex object step by step. Abstract Factory emphasizes a family of product objects (either simple or complex). Builder returns the product as a final step, but as far as the Abstract Factory is concerned, the product gets returned immediately.
  Often, designs start out using Factory Method (less complicated, more customizable, subclasses proliferate) and evolve toward Abstract Factory, Prototype, or Builder (more flexible, more complex) as the designer discovers where more flexibility is needed.

## Slide 14: Limitations
The concept of design patterns has been criticized by some in the field of computer science, because:
Targets the wrong problem
Lacks formal foundations
Leads to inefficient solutions
Does not differ significantly from other abstractions